A Quadratic Model for Piano Tuning

John Lindgren
9 July 2016

Assumption #1: The octave around middle C (or C4) is roughly equal-tempered.
Assumption #2: Due to the inharmonicity of the strings, each octave above or below middle C should be “stretched” incrementally wider than the preceding octave.

Define a “stretch factor” s in semitones per octave. Then each note n, in semitones above middle C, should be tuned s over 2 ( n over 12 ) ^ 2 semitones sharper than equal temperament (and each note below middle C flatter by the same amount).

For my piano, a stretch factor of s = 0.05 semitones (or 5 cents) seems to work well. In other words, the octave around C5 will be tuned 5 cents wider than equal temperament, the octave around C6 will be tuned 10 cents wider, and so on. Using the above formula, we find that each C above and below middle C should be tuned as follows:

C5	5/2 = 2.5 cents sharp	C3	2.5 cents flat
C6	5 + 10/2 = 10 cents sharp	C2	10 cents flat
C7	5 + 10 + 15/2 = 22.5 cents sharp	C1	22.5 cents flat

Now how do we get actual frequencies from this?

In an equal-tempered tuning, the frequency of a note n is x = "C4" cdot 2 ^ { n over 12 } Hz. Adding in our adjustment term, we get x = "C4" cdot 2^{{n + (s over 2) (n over 12)^2} over 12} Hz. (Notes below middle C should be flat rather than sharp, so subtract the adjustment term rather than adding it.)

For concert pitch (A = 440 Hz), the correct frequency for middle C depends on the choice of stretch factor s. Substitute x = 440 Hz and n = 9 semitones in the above formula, then solve for C4. For s = 0.05, the correct frequency is 261.41 Hz.

Plugging that value for C4 back into the formula, we can then compute:

C5	523.58 Hz	C3	130.52 Hz
C6	1051.71 Hz	C2	64.98 Hz
C7	2118.66 Hz	C1	32.25 Hz

The inverse formula n = {24 sqrt{6s log_2 {x over "C4"} + 36} - 144} over s can be used to find the note n which has a frequency of x Hz. (For notes below middle C, replace x over "C4" with "C4" over x and negate n.)